ISSN 1392-3196

Žemdirbystė=Agriculture, vol. 98, No. 3 (2011), p. 323–332

UDK  631.42.05:631.425.5:631.415.2

## Spatial variability of soil pH as influenced by different            soil sampling methods and geostatistical techniques

##### Gediminas STAUGAITIS, Donatas ŠUMSKIS

Agrochemical Research Laboratory

Lithuanian Research Centre for Agriculture and Forestry

Savanorių 287, Kaunas, Lithuania

E-mail: agrolab@agrolab.lt

###### Abstract

The aim of the current research was to assess the spatial variability of mapped soil pH data, obtained from soils of different types, as influenced by soil sampling methods and to evaluate the suitability of different geostatistical methods for the determination of acid areas. pHKCl was measured in soil samples collected from three different sites, located in Elmininkai (155 ha), Daumantiškiai (55 ha) and Dapkūniškiai (73 ha). The following methods of soil sampling were tested: regular grid; soil sampling within the boundaries of prevailing soil group and texture; soil sampling within the boundaries of prevailing soil group and texture and in consideration of previous soil test results. Mapping of acid areas was conducted using IDW, Simple Kriging and Simple Cokriging interpolation methods. Soil samples were collected at 2 ha density.

Our research evidence suggests that the most accurate display of acid areas on the digital map can be obtained when soil sampling is conducted within the boundaries of prevailing soil group and texture and in consideration of previous soil test results. The less detailed display of acid areas was obtained when soil sampling was conducted within the boundaries of prevailing soil group and texture, and the least detailed display when soil samples were collected using the regular grid. As a result of interpolation of pH data using IDW, Simple Kriging and Simple Cokriging methods, the acid areas displayed on the digital maps were significantly smaller than those determined using the not interpolated pH data collected from the fields where acid soils comprised less than one fourth of the area dominated by slightly acid zones, and from the fields where not acid eroded soils intervene the acid zones.

We recommend collecting the soil samples for pH tests within the boundaries of prevailing soil group and texture and in consideration of previous soil test results. The pH data obtained using this soil sampling method may be interpolated employing IDW, Simple Kriging and Simple Cokriging methods only in the cases where acid soils account for more than 50% of the tested area – then the correctness of obtained interpolation results is satisfactory.

Key words: soil sampling, soil pH, interpolation methods.

ISSN 1392-3196

Žemdirbystė=Agriculture, vol. 98, No. 3 (2011), p. 323–332

UDK  631.42.05:631.425.5:631.415.2

### Dirvožemio pH erdvinis pasiskirstymas, taikant skirtingus ėminių atrinkimo būdus ir geostatistinius metodus

##### G. Staugaitis, D. Šumskis

Lietuvos agrarinių ir miškų mokslų centro Agrocheminių tyrimų laboratorija

###### Santrauka

Lietuvoje įvairios dangos dirvožemių pHKCl tyrimai atlikti 2004 m. Anykščių r. Elmininkų (155 ha), Ukmergės r. Daumantiškių (55 ha), 2007 m. – Molėtų r. Dapkūniškių (73 ha) vietovėse. Tikslas – įvairios dangos dirvožemiuose, ėminius imant skirtingais būdais, įvertinti erdvinį pH pasiskirstymą ir geostatistinių metodų taikymą. Siekta įvertinti ėminių paėmimo tinkleliu būdą ir būdus, kai naudojamos dirvožemio grupės bei granuliometrinės sudėties kontūrų ir ankstesnio tyrimo pH kontūrų duomenų bazės. Skaitmeniniame žemėlapyje rūgštiems plotams atvaizduoti taikyti IDW, Sipmple Kriging ir Simple Cokriging interpoliavimo metodai. Dirvožemio ėminiai tyrimams imti 2 ha tankumu.

Tyrimų rezultatai parodė, kad skaitmeniniame žemėlapyje rūgštūs plotai laukuose tiksliausiai atvaizduojami, kai ėminiai atrenkami ir žemėlapyje pateikiami pagal vyraujančio dirvožemio kontūro bei ankstesnio tyrimo rūgščių plotų ribas. Kiek mažiau detaliai rūgštūs plotai atvaizduojami, kai ėminiai imami pagal dirvožemių kontūrų ribas, mažiausiai – taisyklingo tinklelio būdu. Masyvuose, kur rūgštūs plotai sudarė nedidelę dalį (iki ketvirtadalio) viso ploto ir vyravo daugiausia silpnai rūgštaus pH plotai arba kur tarp neeroduotų plotų buvo įsimaišę eroduoti, IDW, Simple Kriging ar Simple Cokriging metodais interpoliuoti pH duomenys pateikė gerokai mažesnį kiekį rūgščių plotų nei neinterpoliuoti.

Rekomenduojama pH tyrimams dirvožemio ėminius imti pagal vyraujančio dirvožemio kontūro ir ankstesnio tyrimo rūgščių plotų ribas. Ėminius imant šiuo būdu, pH duomenų interpoliavimas IDW, Simple Kriging ar Simple Cokriging metodais galimas tik tuomet, kai rūgštūs plotai sudaro daugiau nei 50 % tiriamo ploto. Tokiuose plotuose taikant šiuos interpoliavimo metodus, gaunami panašūs rūgščių plotų rezultatai.

Reikšminiai žodžiai: dirvožemio ėminio ėmimas, dirvožemio pH, interpoliavimo metodai.