ISSN 1392-3196

Žemdirbystė=Agriculture, vol. 99, No. 4 (2012), p. 431–436

UDK  631.5.001.4:629.734

## The suitability of an unmanned aerial vehicle (UAV) for the evaluation of experimental fields and crops

##### Rafal PUDELKO, Tomasz STUCZYNSKI, Magdalena BORZECKA-WALKER

Institute of Soil Science and Plant Cultivation, State Research Institute

Czartoryskich 8, 24-100 Pulawy, Poland

E-mail: rpudelko@iung.pulawy.pl, ts@iung.pulawy.pl, mwalker@iung.pulawy.pl

###### Abstract

The aim of this study was to assess the possibility of monitoring experimental plots by using a remote-controlled flying model adapted to perform low altitude non-metric photographs. In the first part of the paper, the advantages and disadvantages of a moto-glider construction flight as a platform were discussed. The second part presents issues associated with the acquisition and development of photographs taken with this type of construction. The study was conducted in 2008–2010 in the fields of the research farm in Wielkopolska, Poland (N 52.585°, E 16.640°), which belong to the Institute of Soil Science and Plant Cultivation, Pulawy. The photographs were taken over crops of winter wheat, spring barley and maize grown on the plots (size of 36 × 36 m), covering an area of about four hectares. The flights were made at various altitudes (20–700 m above ground level) at selected plant growth stages.

Key words: unmanned aerial vehicle, non-metric aerial photography, remote controlling, “hot patch” detection, distance.

ISSN 1392-3196

Žemdirbystė=Agriculture, vol. 99, No. 4 (2012), p. 431–436

UDK  631.5.001.4:629.734

### Bandymų laukų stebėjimas, naudojant nepilotuojamą motorinį sklandytuvą

##### R. Pudelko, T. Stuczynski, M. Borzecka-Walker

Pulavų valstybinis dirvotyros ir augalininkystės institutas, Lenkija

###### Santrauka

Tyrimo tikslas – įvertinti galimybę stebėti bandymų laukus, naudojant per atstumą valdomą skraidantį modelį, pritaikytą nedideliame aukštyje daryti nemetrines nuotraukas. Straipsnio pirmoje dalyje aptarti motorinio sklandytuvo konstrukcijos privalumai ir trūkumai. Antroje dalyje aptartos problemos, susijusios su tokios konstrukcijos sklandytuvo padarytų nuotraukų kaupimu ir panaudojimu. Tyrimas atliktas 2008–2010 m. Lenkijoje, Vielkopolskos bandymų ūkio laukuose (N 52.585°, E 16.640°), priklausančiuose Pulavų valstybiniam dirvotyros ir augalininkystės institutui. Fotografuoti žieminių kviečių, vasarinių miežių ir kukurūzų pasėlių 36 × 36 m dydžio laukeliai, užimantys 4 hektarų plotą. Skrydžiai atlikti įvairiuose (20–700 m) aukščiuose tam tikrais augalų vystymosi tarpsniais.

Reikšminiai žodžiai: nepilotuojamas skraidantis prietaisas, nemetrinė aeronuotrauka, nuotolinis valdymas, „karštų laukelių“ nustatymas, atstumas.