ISSN 1392-3196

Žemdirbystė=Agriculture, vol. 98, No. 3 (2011), p. 307–314

UDK  631.437.213:[634.11:631.526.32]:631.559

## Determination of the relationship between apparent soil electrical conductivity with pomological properties and yield    in different apple varieties

##### Ufuk TÜRKER, Babak TALEBPOUR, Uğur YEGÜL

Ankara University

Ankara, Turkey

E-mail: uturker@agri.ankara.edu.tr

###### Abstract

Precision horticulture and spatial analysis applied to orchards are a growing and evolving part of precision agriculture technology. The aim of this study was to produce yield and pomological properties maps in order to determine the relationship between these parameters and apparent soil electrical conductivity (ECa) characteristics in different apple varieties, as well as analyze spatial variation in an apple orchard. This study was carried out at an apple orchard in the Faculty of Agriculture of Ankara University’s Haymana Research Station. In this work, apparent soil electrical conductivity values were acquired by using EM38 sensor. These values were used to produce maps and compared with yield and pomological characteristic maps using classical statistics and spatial analyst methods. As a result, the highest value of non-linear regression between ECa and yield was determined in the ‘Red Chief’ (R² = 0.94) while the highest calculated value for yield in cross-sectional area were found to be in ‘Jonagold’ with R² = 0.44. The other indexes such as coefficient of variation and Moran’s I index were used to determine variability and autocorrelation in each value.

# Key words: apparent soil electrical conductivity, yield mapping, pomological properties.

ISSN 1392-3196

Žemdirbystė=Agriculture, vol. 98, No. 3 (2011), p. 307–314

UDK  631.437.213:[634.11:631.526.32]:631.559

###### Išmatuoto dirvos elektrinio laidumo ir ryšio tarp obelų įvairių veislių derliaus pomologinių savybių nustatymas

##### U. Türker, B. Talebpour, U. Yegül

Ankaros universitetas, Turkija

###### Santrauka

Sodams taikoma tikslioji sodininkystė bei erdvinė analizė yra besiplėtojanti ir besivystanti tiksliosios žemdirbystės dalis. Tyrimų tikslas – sudaryti derliaus bei pomologinių savybių žemėlapius, siekiant nustatyti ryšį tarp šių rodiklių ir išmatuoto dirvos elektrinio laidumo (ECa) įvairių veislių obelų savybių, taip pat išanalizuoti erdvinę variaciją obelų sode. Tyrimai atlikti Ankaros universiteto Žemės ūkio fakulteto Haymana tyrimų stoties obelų sode. Tyrimų metu dirvos laidumo vertės išmatuotos EM38 jutikliu. Šie duomenys panaudoti žemėlapiams sudaryti, kurie buvo palyginti su derliaus ir pomologinių savybių žemėlapiais, taikant klasikinius statistinius bei erdvinės analizės metodus. Didžiausia netiesinės regresijos tarp ECa ir derliaus vertė nustatyta veislės ‘Red Chief’ (R² = 0.94), didžiausia apskaičiuota vertė derliui skerspjūvio plote nustatyta veislės ‘Jonagold’ (R² = 0.44). Kiti rodikliai – variacijos koeficientas ir Morano I indeksas – buvo naudojami siekiant nustatyti kiekvienos vertės variaciją ir autokoreliaciją.

# Reikšminiai žodžiai: išmatuotas dirvos elektrinis laidumas, derliaus kartografavimas, pomologinės savybės.